## Slide 1: Sonar
MB1000-LV

## Slide 2: Pin Description

## Slide 3: PW vs AN vs Serial
Burst transmitted – PW set High and echo pulls low
The remainder of the 49mS time (less 4.7mS) is spent adjusting the analog voltage to the correct level. When a long distance is measured immediately after a short distance reading, the analog voltage may not reach the exact level within one read cycle
During the last 4.7mS, the serial data is sent.

## Slide 4: Free Run vs Triggered
Free Run
Pros:
  (3) wires per sensor
  AN: reading not affected since last one is buffered
Cons:
  Multiple sensors will not be synchronized (could range at same time, cross-talk)
  PW: long range time (must wait for the next sensor range event for the PW pin to go LOW-HIGH-LOW)
Triggered
Pros:
  Options: simultaneous, sequential, loop
  PW: decreased read time
Cons:
  (4-5) wires per sensor

## Slide 5: PW vs AN Response Time
AN
PW – free run
Requires non-blocking method

## Slide 6: PW vs AN Response Time
PW – free run
PW – triggered
Requires non-blocking method

## Slide 7: Simultaneous Operation
Pros:
  fastest method
  AN: buffered readings
Cons:
  cross-talk possible
Note: Continuously variable gain – will typically ignore adjacent sensors when running simultaneously.

## Slide 8: Commanded Sequential Operation
Pros:
  PW: each cycle is triggered, no excess time reading PW
  AN: quick buffered response
Cons:
  (6) wires per sensor
  (1) sensor ranging at a time

## Slide 9: Constant Loop Operation
Pros:
  (1) trigger event at setup, continuous loop
  Synchronized, no cross-talk
  AN: quick buffered response
Cons:
  (6) wires per sensor + inline resistor
  (1) sensor ranging at a time
  PW: no control over trigger event, long read times

## Slide 10: Proposed Operation – Individually Triggered Analog Voltage
(1) trigger for each sensor – can control simultaneous / sequential operation via software
Sensor response instantly (AN buffered response)
Function call NO FASTER THAN 50ms (AN will return same buffered value)